Use Case-I

1. User at station.
2. LCD displays 'Welcome to Cykul Station'.
3. And displays to Scan 'Smart Card'.
4. The user will scan card.
5. If the smart card is approved, cycle gets unlocked, LCD displays approved, Red LED will be ON and Green LED will go OFF, Buzzer will beep once.
6. If the smart card is not approved, the procedure follows from step 2 to 5.

Use Case-II

1. User at station.
2. LCD displays 'Welcome to CYKUL Station' for 5 sec then it will display to scan 'Smart Card'.
3. The user will scan his/her Smart Card.
4. If the Smart Card is approved then the LCD displays 'OTP'.
5. The user will enter the PIN through keypad.
6. If the OTP typed by the user is matched, cycle gets unlocked, LCD displays unlocked, Red LED will be ON and Green LED will go OFF, Buzzer will beep once.
7. If the OTP which the user entered is wrong then the procedure starts from step 2 to 6.

Use Case-III

1. User at station.
2. LCD displays 'Welcome to CYKUL Station'.
3. The user will have the downloaded Cykul station app in his/her mobile.
4. The user should Login into the app and give the dock number in mobile.
5. LCD displays to Enter PIN.
6. The registered user will be provided with a PIN at the time of registration.
7. The user will enter the PIN through keypad.
8. If matched, cycle gets unlocked, LCD displays 'Unlocked', Red LED will be ON and Green LED will go OFF and both lights go off to sleepmode , Buzzer will beep once.
9. If the PIN which user entered is wrong then LCD will display Wrong PIN and the procedure starts from step 7 to 8.